## Slide 1
GEO‑AI Sentinel: Real‑Time Disaster Monitoring
Micro‑Patch Streaming + Edge AI on GEO Platforms
31/01/2026

## Slide 2
DOCUMENT TITLE
The Challenge
Existing GEO platforms suffer from high latency and deliver raw data requiring extensive ground processing
Airbus ADS #3 – Fight for our Planet with Airbus Earth Observation data
LEO Limitations
LEO constellations provide fast imaging but cannot continuously monitor the same region
Our Innovation
Cost-effective GEO satellite with Edge AI detecting fires and thermal anomalies within 1–5 minutes

## Slide 3
DOCUMENT TITLE
Performance Barriers
Traditional GEO satellites deliver ~1 km ground pixel resolution, transmitting massive volumes of raw data that overwhelm ground systems and delay critical response times by hours.
Critical Gaps in Current GEO Monitoring
Coarse Resolution
~1 km ground pixel provides insufficient detail for early fire detection
Data Overload
High volumes of raw data create costly transmission and storage requirements
Response Delays
Hours-long processing times reduce disaster response effectiveness
No Intelligence
Lack of onboard processing prevents real-time event identification

## Slide 4
DOCUMENT TITLE
GEO Orbit + Edge AI: A Game-Changing Architecture
1-5
70%
1/3
Minutes to Alert
vs. 1-3 hours with traditional systems
Cost Reduction
Compared to deploying new LEO constellations
Cost Reduction
Compared to deploying new LEO constellations
Our solution combines geostationary positioning with intelligent onboard processing to revolutionize thermal anomaly detection.
Patch Analysis
AI divides full imagery into 1 km² patches for parallel processing
Priority Transmission
Critical patches sent immediately; full imagery transmitted later
Smart Detection
Onboard AI analyzes each patch for thermal signatures and anomalies

## Slide 5
DOCUMENT TITLE
Satellite Platform
Technical Architecture: Proven Platform, Advanced Payload
LWIR Thermal Imaging Payload
Optical System: Catadioptric/Reflective design
Aperture: 250–400 mm
Focal length: 1.5–2.5 m
Materials: Germanium (Ge), Zinc Selenide (ZnSe), DLC coating
Sensor: 640×512 or 1024×1024 microbolometer array
Ground resolution: ~1 km per pixel at GEO
Edge AI Processing: Radiation-hardened SoC/FPGA architecture enables sub-pixel thermal anomaly detection and selective data transmission.

## Slide 6
DOCUMENT TITLE
Optical Physics: Sub-Pixel Fire Detection
Detection Capability
Diffraction Limit: D = 0.25–0.4 m, λ = 10 μm → Ground Spot ≈ 800–1,000 m
Small fire hot spots create measurable temperature increases within larger pixels, enabling sub-pixel detection through thermal signature analysis.
Diffraction Limit
θ ≈ 1.22 λ/D calculation
Ground Spot
800–1000 m spot at GEO
Wavelength
Long-wave IR at 10 μm
Aperture
250–400 mm telescope diameter
The diffraction-limited ground spot size enables detection of thermal signatures significantly smaller than one pixel through thermal analysis.
Location Identification
Pinpoint thermal anomaly presence and coordinates
Early Detection
Identify fires before visible expansion using thermal signatures
Optimized Design
Reduced launch mass and cost through targeted capability

## Slide 7
DOCUMENT TITLE
GEO Orbit Advantages
From 35,786 km altitude, a single satellite provides continuous monitoring of approximately one-third of Earth's surface, extending to ±60° latitude.
Global Coverage with Strategic Priority Zones
Micro-Patch Streaming
Intelligent prioritization ensures high-risk regions receive immediate attention: wildfire zones, protected forests, critical infrastructure, and densely populated urban areas.

## Slide 8
DOCUMENT TITLE
Optimized Optics
LWIR system sized for fire detection with smaller aperture and lower mass
Competitive Advantage vs. Traditional GEO Systems
Simplified Mission
Not a wideband telecom satellite—eliminates high-power transponder requirements
Platform Reuse
Leverage demounted legacy GEO platforms from Airbus inventory
Targeted Capability
No unnecessary multispectral channels—focused thermal detection only

## Slide 9
DOCUMENT TITLE
Payload Breakdown and Mission Budget
LWIR Payload Components
Sensor ($1.2–1.8M): 640×512 or 1024×1024 microbolometer, 17–25 μm pitch, NETD <50 mK
Optics ($0.9–1.6M): Ge/ZnSe materials, DLC coating, 250–400 mm aperture, f/1.5–2.5
Edge AI ($0.8–1.5M): Radiation-hardened SoC/FPGA for onboard processing
Calibration ($0.4–0.7M): Thermal stabilization and sensor calibration systems
Total Payload: $3.3–5.6M | Complete Mission: $140–180M including production, integration, and launch

## Slide 10
DOCUMENT TITLE
Implementation Roadmap
Phase 2: Validation
Conduct comprehensive ground testing and thermal sensor calibration in simulated space environment
1
2
3
4
5
Phase 1: Integration
Integrate LWIR sensor and Edge AI system into legacy GEO Airbus platform, leveraging existing Eurostar architecture
Phase 3: Launch
Deploy via Ariane 6 or Falcon Heavy shared launch to geostationary orbit
Phase 4: Operations
Monitor high-risk regions for thermal anomalies with 1-5 minute alert latency
Phase 5: Expansion
Scale capabilities for floods, volcanic activity, and energy grid monitoring

## Slide 11
THANK YOU
FOR WATCHING
CONTACTS
DOCUMENT TITLE
Nikita Sidiropulo Alekseevich
leftstrice_321@bk.ru
+7 771 353 4885
Check Our Project
Kuanbek Ibragim Askaruli
i.kuanbek@aues.kz
+7 707 686 40 57
Maral Ali
al.maral@aues.kz
+7 706 684 25